# GREETING!

We are grateful for your purchase of our company's VHF/UHF FM Handheld Transceiver. We believe our transceivers, which with slim size, latest fashion design, stabled performance, easy use and powerful function can bring great convenience to your life and work.

# CAUTION:

- Please read this instruction manual carefully before using
this transceiver

- The maintaining of transceiver only can be done by
professional technician

- Do not use the transceiver or charging the battery while
taking on fuel or while parking in a gasoline service station

- Do not expose the transceiver to direct sunlight for a long
time, or place it close to heating appliances

- Do not place the transceiver in excessively dusty areas,
humid areas, wet areas, or on unstable surfaces

- Do not use defective antenna, otherwise this defective
antenna may burn you if it touch your skin

- If an abnormal odor or smoke is detected coming from
the transceiver, turn off the power immediately and remove
the battery pack from the transceiver. Contact our service
station or your dealer.

SAFETY: it is very important for end of user to know the caution for using transceiver

# Professional

# FM Handheld Transceiver

USER'S MANUAL

# USER'S MANUAL

Professional
FM Handheld Transceiver

# UNPACKING AND CHECKING EQUIPMENT

Note: The following unpacking instructions are for use by your dealer,

an authorized service facility, or the factory.
Carefully unpack the transceiver. We recommend that you identify
the items listed in the following table before discarding the packing
material. If any items are missing or have been damaged during
shipment, file a claim with the carrier immediately.

# SUPPLIED ACCESSORIES

| ITEM | QUANTITY |
| --- | --- |
| Antenna | 1 |
| Li-ion Battery Pack (7.4V) | 1 |
| Adapter | 1 |
| Desktop Charger | 1 |
| Belt Clip | 1 |
| User's Manual | 1 |

Adapter

Li-ion Battery Pack

Antenna

User's Manual

Belt Clip

Desktop Charger

# ACCESSORIES PICTURE

# CONTENTS

A. PREPARATION	5

- CHARGING THE BATTERY PACK	  5

- INSTALLING/REMOVING THE BATTERY PACK	5

- INSTALLING THE ANTENNA	  6

- INSTALLING THE BELT CLIP	 6

- INSTALLING THE SPEAKER/MICROPHONE(OPTIQNAL) —  6
B. GETTING ACQUAINTED	7

KEYS AND CONTROLS	7

LCD DISPLAY	10

BASIC TRANSCEIVER MODES	  11

VFO MODE			11

MEMORY RECALL MODE	   11

MENU MODE	  11

C. FEATURES AND OPERATION	  12

(1) BASIC OPERATION	12

SWITCHING POWER ON/OFF	12

ADJUSTING VOLUME	12

ADJUSTING SQUELCH	12

SELECTING FREQUENCY	   13

TRANSMITTING	  13

CHANNEL SETTING	  14

(2)	CTCSS	16

USING CTCSS	  16

STANDARD TONE AND CTCSS TABLE	  17

(3)	MEMORY CHANNELS	18

# Professional

# FM Handheld Transceiver

USERS MANUAL

Professional
USER'S MANUAL    FM Handheld Transceiver

RECALLING MEMORY CHANNELS	18

CLEARING MEMORY CHANNELS	18

CHANNEL DISPLAY FUNCTION	18

INITIALIZING MEMORY	 19

FULL RESET	  19

(4) SCAN	20

SCAN RESUME METHOD	20

SELECTING SCAN RESUME METHOD	20

VFO SCAN	21

MEMORY CHANNEL SCAN	21

LOCKING OUT MEMORY CHANNELS	21

D.	OPERATOR CONVENIENCES	22

KEYPAD LOCK FUNCTION		22

APO (AUTO POWER OFF)	22

TIME-OUT TIMER (TOT)	22

BATTERY SAVER		23

LAMP FUNCTION -	— 23

BEEP FUNCTION	24

STOPWATCH			24

SELECTING AN OUTPUT POWER		24

KEYPAD DIRECT ENTRY	24

FREQUENCY ENTRY		25

MEMORY CHANNEL NUMBER ENTRY	25

CHANGING FREQUENCY STEP SIZE		25

E.	SPECIFICATION	26

# A. PREPARATION

(1) CHARGING THE BATTERY PACK

A . After purchasing or extended storage (more
than 2 months), the battery can not reach its
maximum capacity for the first time recharging.
After repeating the charging/discharging the
battery two or three times, the capacity will reach
its best status.

B Slide the battery pack or the transceiver with the
battery pack into the charger. Make sure the
battery pack contacts are in charging terminals,
the charger LED turn to be yellow and charging
begins. The yellow LED will disappear and turn
to be red if the charging is full.

# Caution:

1.	I! the battery charging is full, do not charge it again. Overcharging will
shorten battery's life or damage it.

2,	If battery charging is correct, but the battery life is shorten so much, please
change the new battery pack.

(2) INSTALLING/REMOVING THE BATTERY PACK

A. Match the two troves of the battery pack with
the corresponding guides on the back of the
transceiver. Slide the battery pack along the
back of the transceiver until you hear *kata*.

# Professional

# FM Handheld Transceiver

USER'S MANUAL

Professional
USER'S MANUAL    FM Handheld Transceiver

B. To remove the battery pack, turn the transceiver off first, then
push the release latch on top and slide the battery pack down.

# B. GETTING ACQUAINTED

# KEYS AND CONTROLS

6, LED Indicator —

- UP Key

- DOWN Key

9. Keypad/ —
Function Key

(3) INSTALLING THE ANTENNA

Hold the base of the supplied antenna, then
screw the antenna into the connector on the
top panel of the transceiver until secure.

(4) INSTALLING THE BELT CLIP

Match the belt clip with the corresponding
grooves on the battery and slide down
the belt clip. Toe remove the belt clip, slide
up the belt clip using you hail or tools.

1. Antenna

-	2. Power/Volume Knob

3. LCD Display

-	    4. Speaker

5. Microphone

- LAMP	17. MIC-SP,

- PTT	Jacks
(Push To Talk)

- Monitor Button

- Battery —
Release
Latch

- Belt Clip

- Battery pack

(5) INSTALLING THE SPEAKER/MICROPHONE(OPTIONAL)

Turn counterclockwise screw
and uncover the Mic's cover,
then Insert the speaker/mic-
rophone plugs into the spea-
ker/microphone jacks.

10. Wirst Loop
Hook	-

# Professional

FM Handheld Transceiver    USER'S MANUAL

# 1. Antenna

Receiving and transmitting the signal

2.	Power/Volume Knob

Turn clockwise to switch on the transceiver, to switch off the transceiver,
turn counterclockwise until a click sounds; Rotate to adjust the volume
level.

3.	LCD Display

Display the transceiver working status

4.	Speaker

Audio Out

5.	Microphone

Voice signal change to be electronic signal

6.	LED Indicator

LED Lights red while transmitting

7.	UP Key

Up to adjust displaying frequency or modify the feature

8. Down Key

Down to adjust displaying frequency or modify the feature

Professional
USER'S MANUAL    FM Handheld Transceiver

9.	Keypad/Function Key

Used to input the frequency and setting function

10.	Wrist Loop Hook

Use to fix the wrist Loop

11.	Battery Release Latch

Used to fix or remove the battery

12.	Belt Clip

Easy to carry and used to fix the transceiver to belt

13.	Battery Pack

Supply the power to transceiver

14.	Lamp

Press to light the back lit and keypad light

15.	PTT (Push To Talk)

To make a call, press and hold the PTT button, then speak into the
microphone with normal invoice. Release the PTT to receive.

16.	Monitor Button

Press the button for closing the SQUELCH and release for open

17. MIC-SP Jacks

.    If desired, connect a speaker-microphone here

# Professional

FM Handheld Transceiver    USER'S MANUAL

# LCD DISPLAY

In LCD screen, displays all kinds of symbol, different symbol different
meaning, please see below table, it will helpful for your operation

|  | Appears when the function key is pressed. |
| --- | --- |
|  | S-meter (RX) and relative RF power meter (TX). |
|  | Appears when the transmit output power is set to Low. |
|  | Shows the battery life. |
|  | Appears when the displayed memory channel has been locked out. |
|  | Appears when the memory channel contained data. |
|  | Display the current memory channel when in Memory Recall mode. |
|  | Display various alphanumeric information such as an operating channel or menu selection. |
| APO | Appears when the Auto Power Off function is activated. |
| CT | "CT" appears when the CTCSS function is activated. |
|  | Appears when the Frequency Shift function is activated |
|  | Appears when the,key unlock function is activated. |
|  | Appears when the Lock function is ON. |

Professional
USER'S MANUAL    FM Handheld Transceiver

# BASIC TRANSCEIVER MODES

This section introduces you to the basic modes you can select on this
transceiver.

1. VFO MODE

Pressto select. In this mode you can change the operating

frequency by using the

2.	MEMORY RECALL MODE

Pressto select. In this mode you can change memory channels,
using the      , where you stored frequencies and related data.

You cannot enter this mode unless you program one memory channel
at least. For further information, refer to "MEMORY CHANNELS".

3.	MENU MODE

Presscombine with other key to select. In this mode you can

change the setting by using the

10

11

Professional
FM Handheld Transceiver

USER'S MANUAL

a. Press

* The current squelch level appears.

# Professional

FM Handheld Transceiver    USER'S MANUAL

# C. FEATURES AND OPERATION

(1) BASIC OPERATION

# SWITCHING POWER ON/OFF

1.	Turn the [POWER] switch clockwise to turn ON the transceiver.

•	A music tone sounds.

2.	To turn OFF the transceiver, turn the [POWER] switch counter-
clockwise again.

•	The transceiver stores the parameters when it is turned OFF. It
recalls these parameters next time you turn the transceiver ON
again.

# ADJUSTING VOLUME

Turn the [VOLUME] control clockwise to increase
the audio output level and counterclockwise
to decrease the output level.

•	If you want to check whether there is interfer-
ence on this channel, please press (Moni)

button and turn (VOL), then you will hear the squelch or interference
sounds.

# I ADJUSTING SQUELCH

The purpose of the Squelch is to mute the speaker when no signals
are present. With the squelch level correctly set, you will hear sound
only while actually receiving signals. The higher the selected squelch
level, the stronger the signals must be, to receive. The appropriate
squelch level depends on the ambient RF noise conditions.

12

b.	Use the,key to select the squelch level from 0 to 9.

- Select just the level at which the background noise is eliminated
when no signal is present.

- The larger the level number you select, the stronger the signals
you need to receive to hear.

c.	Press any key other than [LAMP] and [MONI] to complete the
setting.

# I SELECTING FREQUENCY

Usekey to increase the frequency, andto decrease the
frequency.

•	If you cannot select a particular frequency, the frequency step size
needs to be changed. See "CHANGING FREQUENCY STEP SIZE".

•	You can also select frequencies with the numeric keys.

# I TRANSMITTING

a. To transmit, hold the transceiver approximately 5 cm (2 inches)
from your mouth, then press and hold the [PTT] switch and speak
into the microphone in your normal tone of voice.

•	The status LED on the top panel lights red and bar-graph meter
appears

13

# Professional

# FM Handheld Transceiver

USER'S MANUAL

# USERS MANUAL

Professional
FM Handheld Transceiver

b. When you finish speaking, release the [PTT] switch.
Note: If you transmit continuously for more than 4 minutes, the
internal time-out timer generates a warning beep and the transceiver
stops transmitting. In this case, release the [PTT] switch and let
the transceiver cool down for a while, then press the [PTT] switch
again to resume transmitting.

# CHANNEL SETTING

Presskey, LCD display to (CH-001 01).

Press [MONI] andkey, then power ON, enter to self programming
mode. LCD display (SELF),

Start to enter programming mode. Please presskey to start

to set, then you can enter to submenu.

a. Selecting Channel

Useorkey to select your desired channel, range from
1-199, LCD display to (CH-001 01).

b.	RX Frequency Setting

Press [PTT], thenkey to enter RX frequency setup. You can

select your RX frequency through keypad/Function Key, after press
[PTT] to complete the setting.

• To change the channel spacing, presskey to switch between
5KHz and 6.25KHz.

c.	RX CTCSS Setting

When you enter this mode, LCD display (oFF 3). Presskey to

enter, useorkey to select your desired CTCSS frequency
(50 groups of CTCSS available), press [PTT] to complete the setting.

d.	TX Frequency Setting

Same with RX Frequency setup.

e.	TX CTCSS Setting

Same with RX CTCSS setup.

f.	Beat Shift Setting

Useorto switch between ON and OFF
(Default setting OFF).

g.	Scan Del/Add Setting

Useorto switch between Add (Add Scan, Default setting)

and dEL (Scan Delete),

h. TX Power Hi/Lo Select

Useorto switch between Hi (High Power Output, default

setting) and Lo (Low Power Output),

i. Complete self programming mode, LCD display (End 09).

Press [PTT] to enter to next channel setting.

14

15

# Professional

FM Handheld Transceiver    USER'S MANUAL

# (2) CTCSS

You may sometimes want to hear calls from only specific persons or
groups. The Continuous Tone Coded Squelch System (CTCSS) allows
you to ignore (not hear) unwanted calls from other persons who are
using the same frequency. Simply select the same CTCSS tone as
selected by the other persons in your group. A CTCSS tone is sub-
audible tone and is selectable from among the 50 tone frequencies.
Note: CTCSS does not cause your conversation to be private. It only
relieves you of listening to unwanted conversations.

■ USING CTCSS

a.	Select the desired channel number.

b.	Press,to switch the CTCSS function ON (or OFF).
• "CT" appears on left top of the LCD when CTCSS is ON.

Professional
USER'S MANUAL    FM Handheld Transceiver

d.	Use,to select a tone frequency.

e.	Press [PTT] to complete the setting.

■ STANDARD TONE AND CTCSS TABLE

| CTCSS Frequency (Hz) |
| --- |
| 67.0 | 69.3 | 71.9 | 74.4 | 77.0 | 79.7 | 82.5 | 85.4 | 88.5 |
| 91.5 | 94.8 | 97.4 | 100.0 | 103.5 | 107.2 | 110.9 | 114.8 | 118.8 |
| 123.0 | 127.3 | 131.8 | 136.5 | 141.3 | 146.2 | 151.4 | 156.7 | 159.8 |
| 162.2 | 165.5 | 167.9 | 171.3 | 173.8 | 177.3 | 179.9 | 183.5 | 186.2 |
| 189.9 | 192.8 | 196.6 | 199.5 | 203.5 | 206.5 | 210.7 | 218.1 | 225.7 |
| 229.1 | 233.6 | 241.8 | 250.3 | 254.1 |  |  |  |  |

c. Press

• The current CTCSS frequency appears.

16

17

# Professional

FM Handheld Transceiver    USER'S MANUAL

USERS MANUAL

Professional
FM Handheld Transceiver

(3) MEMORY CHANNELS

# RECALLING MEMORY CHANNELS

a. Pressto enter Memory Recall mode.

• The memory channel used last is recalled.

b. Use,to select the desired memory channel.

- You cannot recall empty memory channels.

- To restore VFO mode, pressagain.

# CLEARING MEMORY CHANNELS

a.	Enter Self Programming Mode, select the channel you want to
clear.

b.	Press [PTT] to next step, LCD display the current RX Frequency,
pressto clear.

c.	Press [PTT] to complete the setting.

# CHANNEL DISPLAY FUNCTION

When this function is switched ON, the transceiver displays only a
memory channel number instead of a frequency.
1. Pressand then switch power ON to switch this function ON
(or OFF).

# INITIALIZING MEMORY

If your transceiver seems to be malfunctioning, initializing the
transceiver may resolve the problem.

Remember that you need to re-program memory channels after
initialization. On the other hand, initialization is a quick way to clear
all memory channels.

# FULL RESET

Use to initialize all settings.

1. Pressthen Power ON the transceiver.

• A confirmation message appears.

• To quit resetting, press any key other than
2. Pressagain.

# 18

19

# Professional

FM Handheld Transceiver    USER'S MANUAL

USER'S MANUAL

Professional
FM Handheld Transceiver

# D. OPERATOR CONVENIENCES

■	KEYPAD LOCK FUNCTION

The Lock function disables most of the keys to prevent you from
accidentally activating a function.

a.	Press(1 second).

•	Appears when this function id ON.

b. Press ( second) to unlock the keys.

c.Keys enable

Sometimes you would like to usekey to change the memory

channel when the keypad lock function is ON, you can unlock the
 key to function even the keypad lock function is ON.

•	Pressto activate,"— " Appears.

■	APO (AUTO POWER OFF)

The transceiver switches OFF automatically if no keys and controls '
are pressed or adjusted, and no signal is received for 2 hours. 1
minute before the transceiver switch OFF, warning beeps sound for
few seconds and "A" blinks. Then, the transceiver turns OFF
automatically.

a.	Pressto switch ON the APO.

•	" APO " appears.

b.	To OFF the APO, pressagain.

■	TIME-OUT TIMER (TOT)

The TIME-OUT Timer (TOT) limits the time of each transmission. The
built-in time-out timer limits each transmission time to a maximum
of 7 minutes. Just before the transceiver stops the transmission, a

warning beeps sounds. It is necessary to protect the transceiver
from thermal damage. You can turn this function OFF.
a. Pressto enter the TOT menu mode.

- Presskey to select your desired time (from 1 -7 minutes)
or switch it OFF.

- If your transmitting time is longer than Tot’s time (factory default
time is 4 minutes), transceiver will stop to transmit and sounds "Bi".
To stop "Bi" sounds, release [PTT] Key and start to transmit again.

# BATTERY SAVER

Battery Saver extends the operating time of the transceiver. It
automatically activates when the squelch is closed and no key is
pressed for more than 5 seconds. To reduce the battery consumption,
it shuts the receiver circuit OFF for the programmed time then
momentarily turn it back ON to detect a signal. To program the
receiver shut-off period for battery saver,
a. Pressto switch the Battery Saver ON/OFF

•	When the Battery Saver ON,appears.

# LAMP FUNCTION

You can illuminate the transceiver display by pressing [LAMP].
Approximately 5 seconds after releasing [LAMP], the light goes OFF
if no other key is pressed. Pressing any key other than [LAMP] while
the display is lit restarts the 5 second timer; pressing [LAMP] turns
OFF the light immediately.

a. To latch the light ON, press, [LAMP]. The light remains ON

until you press, [LAMP] again.

22

23

# Professional

# FM Handheld Transceiver

USERS MANUAL

# USER'S MANUAL

Professional
FM Handheld Transceiver

# I BEEP FUNCTION

The Beep function provides you confirmation of entry, error status,
and malfunctions of the transceiver. We recommend you leave it ON
in order to detect erroneous operations and malfunctions.
However, to turn the Beep function OFF:

a.	Pressto enter the Beep menu mode.

b.	Pressorkey to switch between ON/OFF.

c.	Press any key other than [LAMP] and [MONI] to complete the
setting.

# I STOP WATCH

This is an additional function for your convenience.

a.	Pressto starts the counting.

b.	To stop, presskey, presskey again to restart. Press
any other key to quit other than [LAMP]and [MONI].

# I SELECTING AN OUTPUT POWER

Selecting lower transmission power is the best way to reduce the
battery consumption, if communication is still reliable. You can
configure different power levels for transmission,
a. Presskey to switch between high and low output power,

when you switch to low output power status,symbol displays

in LCD.

# KEYPAD DIRECT ENTRY

You can select the desired operating frequency or memory channel
by entering digits directly from the keypad. Enter the next digit within
10 seconds.

# FREQUENCY ENTRY

a.	Pressto select VFO mode.

b.	Press the numeric keys in sequence on the keypad.
Note:

- When the current step size is 5kHz, the 1 kHz digit is corrected
according to which key is pressed for the 1 kHz digit. Pressing [0]
~ [4] selects "0" and pressing [5] ~ [9] selects 5.

- When the current step size is 12.5 kHz, the 1 kHz and subsequent
digits are corrected according to which keys are pressed for the
10 KHz and 1 kHz digits.

# MEMORY CHANNEL NUMBER ENTRY

a.	Pressto enter Memory Recall mode.

•	The memory channel used last is recalled.

b.	Press the numeric keys to enter a 2-digit memory channel number.

- To recall channel 3, for example, enter "03".

- Do not enter a memory channel number with no any data stored.

# I CHANGING FREQUENCY STEP SIZE

Choosing the correct step size is essential in order to select your
exact receive frequency.

a.	Pressto select VFO mode.

b.	Pressswitch between step size 5, 10, 12.5, 25kHz.
Note: Changing between step size may correct the displayed
frequency. For example, if 150.525 MHz displayed with a 12.5 kHz
step size selected,   changing to a 25 kHz step size corrects the
displayed frequency to 150.510 MHz.

24

25

# Professional

FM Handheld Transceiver    USER'S MANUAL

Professional
USER'S MANUAL    FM Handheld Transceiver

# E. SPECIFICATION

*Specifications are subject to change for improvements without notice.

26

27

# Professional

FM Handheld Transceiver    USER'S MANUAL

Professional
USER'S MANUAL    FM Handheld Transceiver

# E. SPECIFICATION

| GENERAL |
| --- |
| Frequency Range | 136-174MHz |
| Working Temperature Range | -10°C~+60°C |
| Frequency Mode | PLL Frequency |
| Channel Space | 12.5/25Khz |
| Power Supply | DC7.4V (Li-ion Battery 1100 Mah) |
| Memory Channel | 199 Channels |
| Antenna | Rubber Antenna |
| Antenna Impedance | 50 Om |
| Working Mode | Same Frequency Simplex Operation Or Different Frequency Simplex Operation |
| Dimension | 93*50*23.5mm(Do Not Include Antenna) |
| Weight | About 230g |
| RECEIVING |
| Sensitivity | <0.20 mkV (12dB SINAD) |
| Squelch Sensitivity | <O.2 mkV |
| Inter modulation Interference Resistance | >60dB |
| Audio Power | >= 400mW |
| Receiving Current | < 140mA |
| Standby Current | 20mA |

| TRANSMITTING |
| --- |
| Output Power | 5W/1W |
| Modulation Mode | 16KOF3E FM |
| Max. Frequency Division | <=±5KHz |
| Spurious Radiation | <-70dB |
| Reemphasis Character | 6dB |
| Emission Current | HI:<1.5A LO:<0.8A |

*Specifications are subject to change for improvements without notice.

26

27