Installation

- Place the video memory unit to the left surface of monitor station

- Slide the video memory unit in the direction of forward

Put the connection cable into the socket on the bottom of monitor as shown

Operation

Panel(HVM-300B/HVM-300C)

Time Setting

After the screen on the monitor turns on, the time information will appear on the screen. Select and adjust "Hour" and "Minute" you want. The default time display (factory setting) is "12:00"(HVM-300B)/"01/01/2004 THU 12:00"(HVM-300C).

HVM-300B

- Press Monitor button (0) to turn on the screen.

- The current time information will be displayed on the screen.

- Press Time button to select "Hour". The "Hour" on the screen will blink.

- Press Record button or Review button to scroll up or down and then select "Hour" you want.

- Press Time button again. The "Minute" on the screen will blink.

- Press Record button or Review button to scroll up or down and then select "Minute" you want.

- Press Time button to end time setting mode.

HVM-300C

- Press Time button

- The current month, day, year, time information will be displayed on the screen.

- Press Record button or Review button to scroll up or down and then select "Month" you want.

- Press Time button again. The "Date" on the screen will blink.

- Press Record button or Review button to scroll up or down and then select "Date" you want.

- Please repeat previous steps to complete other "Year", "Day", "Hour" and "Minute" settings.

- Press Away button to end time setting mode.

Picture Save

The visitor image on the screen can be stored manually or automatically on absence mode.

A. Manual picture save mode

You can save picture on the screen manually using Record button.

- The image will appear on the screen after Call button on the door camera or monitor button) on the monitor is pressed.

- Press Record button to save picture on the screen.

P01 (HVM-300B)/ PAGE 01 (HVM-300C) will be displayed on the screen.

- Press Record button to save another picture on the screen.

"P02" (HVM-300B)/ "PAGE 02" (HVM-300C) will be displayed on the screen.

- In this way, you can save up to 64 pictures (HVM-300B) / 60 pictures(HVM-300C)

(P00 → P01 → P02 → Р03 → ... → P62 → P63) (model: HVM-300B)

(PAGE 00 → PAGE 01 → PAGE 02 → .... → PAGE 58 → PAGE 59) (model: HVM-300C)

- It starts overwriting previous recorded pictures after you save more than 64 pictures (HVM-300B) / 60 pictures(HVM-200C)

- If more than 5 seconds elapse after you press Record button, the screen on the monitor will turn off automatically.

B. Automatic picture save mode during absence)

Set the absence picture save mode when you leave home. If Call button on the door camera is pressed during your absence, the picture on the monitor will be stored automatically.

- Press Away button before you leave home

- The LED lamp of image memory unit will flash.

- The visitor image will be saved automatically after door camera calls.

- To end the absence picture save mode, press Away button again.

Review

- To view recorded pictures, press Review button.

- The latest saved picture will be displayed on the screen.

- Press Review button again to move next picture saved.

- To end review mode, press Away button.

Specifications

HVM-300B/HVM-300C

| Items | Specifications |
| --- | --- |
| Power Consumption | HVM-300B | Max 3W (supplied power from HA-300/HAC-300) |
|  | HVM-300C | Max 4.1 W (supplied power from HA-300/HAC-300) |
| Resolution | HVM-300B | 256X240 (EIA), 256X256 (CCIR) |
|  | HVM-300C | 360X240 (NTSC), 360X288 (PAL) |
| Image Memory | HVM-300B | Max. 64 Pics |
|  | HVM-300C | Max. 60 Pics |
| Size | Dimension | 68.1 W x 210 H x 53.9 D (mm) 2.68 W x 8.27 H x 2.12 D (lnches) |
|  | Weight | 0.23 kg /0.51 Ibs |
| RTC Error Rate | HVM-300B | ± 150 usec / 1 sec ( ± 12.96 sec/ 1 day) |
|  | HVM-300C | ± 20 usec/ 1sec (± 630.72 sec/ 365day) |
| RTC Discharge Time | HVM-300C | 216 Hours (9day ± 1day) |
| Installation | Compatible to HA-300/ HAC-300 |

Warranty Conditions

HYUNDAI TELECOM Products are supplied with one (1) year return to base warranty from the date of purchase. We will repair or replace the defective item with a new or factory rebuilt replacement.

Condition

- This warranty applies to the original purchaser only.

- All warranty will be invalid if unauthorized repair or modification are made to the unit or in any case of accident, misuse, damage caused by improper installation and altered serial numbers.

- The liability of HYUNDAI TELECOM is limited to the cost of repair/replacement of the unit under warranty.

- If you need a warranty service, you should send the product to our customer service Dep't or dealer office. The product in all cases must be accompanied by the following items:

Your name, address, telephone number, the serial number, copy of your sales receipt showing the purchase date.

The Model Number is on the box and front of the manual. The Serial Number is on the bottom of the unit. Record the Model and Serial Numbers in the spaces provided below. Refer to these numbers for warranty service.